## Slide 1: Section 2
Systems Programming ECE3502

## Slide 2: SIC machine architecture
Memory
it consists of 8-bit bytes
3 consecutive byte from a word(24 bits)
Data Formats
Integers are stored as 24-bit binary numbers
2’S complement representation is used for negative values
Total of 32768 (2^15) bytes in the computer memory
Characters are stored using their 8-bit ASCII codes
No floating-point hardware on the standard version of sic
Notes: Remember memory size is 2 to the power 15 bytes

## Slide 3: SIC machine architecture
Instruction formats
  24-bit format
  X is to indicate index-address mode
  Addressing modes
LDA ALPHA  MEMORY[ALPHA]
LDA ALPHA,X  MEMORY[ALPHA+X]
Notes: Remember memory size is 2 to the power 15 bytes

## Slide 4: Assembler Directives
Pseudo-Instructions
Not translated into machine instructions
Providing information to the assembler
Basic assembler directives
START: Specify name and starting address for the program
END: Indicate the end of the source program, and (optionally) the first executable instruction in the program.
BYTE: Generate character or hexadecimal constant, occupying as many bytes as needed to represent the constant.
WORD: Generate one-word integer constant
RESB: Reserve the indicated number of bytes for a data area
RESW: Reserve the indicated number of words for a data area

## Slide 5: Assembler Data Structures
Operation Code Table (OPTAB)
Symbol Table (SYMTAB)
Location Counter (LOCCTR)

## Slide 6
Pass One

## Slide 7
Pass One
Symbols Instructions Reference
Location Counter
0000
0000
0000+3=0003
0009+3=000C
0003+3=0006
0015+3=0018
000C+3=000F
0006+3=0009
000F+3=0012
0012+3=0015
001B+3=001E
0018+3=001B
001E+3=0021
0021+3=0024
0150+3=0153
0153+3=0156
0024+(100*3)10 = 0150
0156+3=0159
Symbol | Address
Prog1 | 0000
Loop | 0006
Index | 0021
Alpha | 0024
Zero | 0150
K300 | 0153
Three | 0156
Twenty | 0159
Symbol Table
0159+3=015C
Translate (by hand) the following assembly program to SIC object code. Which contains H record, T record, and E record.
Sheet 2 Question 1

## Slide 8
Pass Two
Symbols Instructions Reference
Location Counter
0000
0000
0003
000C
0006
0018
000F
0009
0012
0015
001E
001B
0021
0024
0153
0156
0150
0159
Obj. Code
No obj. code
000150
0C0021
015C
LDA ZERO |  | 
Address (15bits) | X | Opcode (8)
0150 | 0 | 00
0000 0001 0101 0000 | 0 | 0000 0000
0150 |  | 00
STA INDEX |  | 
Address (15bits) | X | Opcode (8)
0021 | 0 | 0C
0000 0000 0010 0001 | 0 | 0000 1100
0021 |  | 0C
Question 1

## Slide 9
Pass Two.
Symbols Instructions Reference
Location Counter
0000
0000
0003
000C
0006
0018
000F
0009
0012
0015
001E
001B
0021
0024
0153
0156
0150
0159
Obj. Code
No obj. code
000150
0C0021
0C8024
040021
28 0153
00 0021
000150
18 0156
0C 0021
38 0006
2C 0159
000064
000003
000000
000014
015C
LDX INDEX |  | 
Address (15bits) | X | Opcode (8)
0021 | 0 | 04
0000 0000 0010 0001 | 0 | 0000 0100
0021 |  | 04
STA ALPHA, X |  | 
Address (15bits) | X | Opcode (8)
0024 | 1 | OC
0001 0000 0010 0100 | 1 | 0000 1100
8024 |  | 0C
No obj. code
No obj. code
No obj. code
Question 1

## Slide 10
Pass Two..
H.T.E Record
H. program name(6). Starting address(6). Length(6)
H.XXProg1.000000.00015C
T. Starting address of each t record(6) . Size of instruction(2). obj. code of all inst(6)
T.000000.1E.000150.0C0021.040021.000150.0C8024.00021.180156.0C0021.280153.2C0159
T.00001E.03.380006
T.000150.0C. 0000000.000064.0000003.000014
E. Starting address(6)
E.000000
Question 1

## Slide 11
More Examples
Obj. Code | Reference | Instructions
BYTE X ’05’
05
BYTE C ’EOF’
454F46

## Slide 12
PASS ONE & TWO
 |  |  |  | Location Counter
Symbols Instructions Reference
Obj. Code
0030
0030
0039
0036
0033
003C
003F
0045
0042
004B
0048
00B0
004C
No Obj. code
No Obj. code
No Obj. code
04 0045
E0 004B
30 0033
50 804C
DC 004B
2C 0048
38 0033
000000
000001
05
Address | Symbol
WRREC 0030
WLOOP 0033
ZERO 0045
LENGTH 0048
OUTPUT 004B
RECORD 004C
H.HW1BXX.000030.000080
E.000030
T.000030.1C.
040045.E0004B.300033.
50804C.DC004B.2C0048.380033.000000.
000001.05
Question 2