## Slide 1: Section 4
Systems Programming ECE3502

## Slide 2
Memory formats
1 megabytes (2^20 bytes)
Registers
There are nine registers; each register is 24 bits in length except floating point register
Number
0
1
4
5
6
8
9
3
2
SW
Status Word
24
24
SIC/XE Machine Architecture

## Slide 3: Instruction formats
Example: TIO
Example: ADDR S,T
Example: LDA #3
Example: +JSUB RDREC
Notes: Remember memory size is 2 to the power 15 bytes

## Slide 4
SIC/XE Addressing Modes

## Slide 5: Sheet3, Q1)
Given the following memory structure calculate the target address and find the value loaded into register A for the following machine instructions:
032600
03C300
opcode | n | i | x | b | p | e | Disp.
1 Get address: (b,p,x)
TA=disp+ (PC)
TA=600+3000
2 Use address: (n,i)
TA=3600
Value=(TA)= (3600)
Value=103000
opcode | n | i | x | b | p | e | Disp.
1 Get address: (b,p,x)
TA=disp+ (B)+ (x)
TA=300+6000+90
2 Use address: (n,i)
TA=6390
Value=(TA)= (6390)
Value=00C303
0000 00 1 1
0 0 1 0
0110 0000 0000
0000 00 1 1
1 1 0 0
0011 0000 0000
Notes: Remember memory size is 2 to the power 15 bytes

## Slide 6: Sheet3, Q1)
022030
010030
opcode | n | i | x | b | p | e | Disp.
1 Get address: (b,p,x)
TA=disp+ (PC)
TA=030+3000
2 Use address: (n,i)
TA=3030
Value=((TA))= ((3030))
Value= (3600) = 103000
opcode | n | i | x | b | p | e | Disp.
1 Get address: (b,p,x)
TA=disp
TA= 030
2 Use address: (n,i)
TA=030
Value=TA= 030
Value=000030
0000 00 1 0
0 0 1 0
0000 0011 0000
0000 00 0 1
0 0 0 0
0000 0011 0000
Notes: Remember memory size is 2 to the power 15 bytes

## Slide 7: Sheet3, Q1)
0310C303
opcode | n | i | x | b | p | e | Add.
1 Get address: (b,p,x)
TA=address
TA=0C303
2 Use address: (n,i)
TA= 0C303
Value=(TA)= (0C303)
Value=003030
0000 00 1 1
0 0 0 1
0000 1100 0011 0000 0011
003600
opcode | n | i | x | b | p | e | Add.
1 Get address: (b,p,x)
TA=address
TA=3600
2 Use address: (n,i)
TA= 3600
Value=(TA)= (3600)
Value=103000
0000 00 0 0
0 0 1 1
0110 0000 0000
Opcode(8) |  |  | x | Address(15)
0000 0000
0
011011000000000
Notes: Remember memory size is 2 to the power 15 bytes