## Slide 1: Section 7
Systems Programming ECE3502

## Slide 2
SIC-XE DISASSEMBLER
HPROG1X00100000001D
T0010001DB410B400B44075101000E32019332FFADB2013A00433200857C003B850
E001000
Given the following necessary information:
AND
Assume B=101A
NOTE THAT: This HTME is not covering the whole program
Instruction | Opcode | Format
CLEAR r1 | B4 | 2
LDT | 74 | 3/4
TD | E0 | 3/4
RD | D8 | 3/4
JEQ | 30 | 3/4
COMPR r1,r2 | A0 | 2
STCH | 54 | 3/4
TIXR r1 | B8 | 2
Notes: Remember memory size is 2 to the power 15 bytes

## Slide 3
HPROG1X00100000001D
T0010001DB410B400B44075101000E32019332FFADB2013A00433200857C003B850
E001000
Assume that the instruction is format 3 so we are going to take 6 hexadecimal
1st instruction:
B410B4
Since n=0 & i=0, then the instruction is neither format 3 nor format 4
B4 op code => CLEAR (format 2) 1st instruction:
B410
CLEAR X
Op code | ni xbpe | Disp
1011 01 | 00 | 
Op code | R1 | R2
1011 0100 | 0001 | 0000
 | PROG1 | Start | 1000 | -----------
1000 |  |  |  | 

## Slide 4
HPROG1X00100000001D
T0010001DB410B400B44075101000E32019332FFADB2013A00433200857C003B850
E001000
Assume that the instruction is format 3 so we are going to take 6 hexadecimal
2nd instruction:
B400B4
Since n=0 & i=0, then the instruction is neither format 3 nor format 4
B4 op code => CLEAR (format 2) 2nd instruction:
B400
CLEAR A
Op code | R1 | R2
1011 0100 | 0000 | 0000
 | PROG1 | Start | 1000 | -----------
1000 |  | CLEAR | X | B410
1002 |  |  |  | 
Op code | ni xbpe | Disp
1011 01 | 00 | 

## Slide 5
HPROG1X00100000001D
T0010001DB410B400B44075101000E32019332FFADB2013A00433200857C003B850
E001000
Assume that the instruction is format 3 so we are going to take 6 hexadecimal
3rd instruction:
B44075
Since n=0 & i=0, then the instruction is neither format 3 nor format 4
B4 op code => CLEAR (format 2) 3rd instruction:
B440
CLEAR S
Op code | R1 | R2
1011 0100 | 0100 | 0000
 | PROG1 | Start | 1000 | -----------
1000 |  | CLEAR | X | B410
1002 |  | CLEAR | A | B400
1004 |  |  |  | 
Op code | ni xbpe | Disp
1011 01 | 00 | 

## Slide 6
HPROG1X00100000001D
T0010001DB410B400B44075101000E32019332FFADB2013A00433200857C003B850
E001000
Assume that the instruction is format 3 so we are going to take 6 hexadecimal
4th instruction:
751010
Since n=0 & i=1, then immediate #
Since e=1 => format 4 +
4th instruction:
75101000
Op code => return discarded bits
74 op code => LDT
+LDT #4096
Op code | ni xbpe | Disp
0111 01 | 01 0001 | hexa (01000)
Op code | ni xbpe | Address
0111 0100 | 01 0001 | hexa (01000)
Address value in decimal
 | PROG1 | Start | 1000 | -----------
1000 |  | CLEAR | X | B410
1002 |  | CLEAR | A | B400
1004 |  | CLEAR | S | B440
1006 |  |  |  | 

## Slide 7
HPROG1X00100000001D
T0010001DB410B400B44075101000E32019332FFADB2013A00433200857C003B850
E001000
Assume that the instruction is format 3 so we are going to take 6 hexadecimal
5th instruction:
E32019
Since n=1 & i=1, then direct
Since e=0 => format 3
Since b=0 & p=1, then PC relative
TA= disp+PC = 019+100D = 1026
Op code => return discarded bits
E0 op code => TD
TD Ref1
Op code | ni xbpe | Disp
1110 00 | 11 0010 | hexa (019)
Op code | ni xbpe | Disp
1110 0000 | 11 0010 | hexa (019)
 | PROG1 | Start | 1000 | -----------
1000 |  | CLEAR | X | B410
1002 |  | CLEAR | A | B400
1004 |  | CLEAR | S | B440
1006 |  | +LDT | #4096 | 75101000
100A |  |  |  | 
Symbol | Address
Ref1 | 1026

## Slide 8
 | PROG1 | Start | 1000 | -----------
1000 |  | CLEAR | X | B410
1002 |  | CLEAR | A | B400
1004 |  | CLEAR | S | B440
1006 |  | +LDT | #4096 | 75101000
100A |  | TD | Ref1 | E32019
100D |  |  |  | 
HPROG1X00100000001D
T0010001DB410B400B44075101000E32019332FFADB2013A00433200857C003B850
E001000
Assume that the instruction is format 3 so we are going to take 6 hexadecimal
6th instruction:
332FFA
Since n=1 & i=1, then direct
Since e=0 => format 3
Since b=0 & p=1, then PC relative
TA= disp+PC = FFFFFFA+1010 = 100A
Op code => return discarded bits
30 op code => JEQ
JEQ Ref2
Op code | ni xbpe | Disp
0011 00 | 11 0010 | hexa (FFA)
Op code | ni xbpe | Disp
0011 0000 | 11 0010 | hexa (FFA)
Symbol | Address
Ref1 | 1026
Ref2 | 100A

## Slide 9
 | PROG1 | Start | 1000 | -----------
1000 |  | CLEAR | X | B410
1002 |  | CLEAR | A | B400
1004 |  | CLEAR | S | B440
1006 |  | +LDT | #4096 | 75101000
100A | Ref2 | TD | Ref1 | E32019
100D |  | JEQ | Ref2 | 332FFA
1010 |  |  |  | 
HPROG1X00100000001D
T0010001DB410B400B44075101000E32019332FFADB2013A00433200857C003B850
E001000
Assume that the instruction is format 3 so we are going to take 6 hexadecimal
7th instruction:
DB2013
Since n=1 & i=1, then direct
Since e=0 => format 3
Since b=0 & p=1, then PC relative
TA= disp+PC = 013+1013 = 1026
Op code => return discarded bits
D8 op code => RD
RD Ref1
Op code | ni xbpe | Disp
1101 10 | 11 0010 | hexa (013)
Op code | ni xbpe | Disp
1101 1000 | 11 0010 | hexa (013)
Symbol | Address
Ref1 | 1026
Ref2 | 100A

## Slide 10
 | PROG1 | Start | 1000 | -----------
1000 |  | CLEAR | X | B410
1002 |  | CLEAR | A | B400
1004 |  | CLEAR | S | B440
1006 |  | +LDT | #4096 | 75101000
100A | Ref2 | TD | Ref1 | E32019
100D |  | JEQ | Ref2 | 332FFA
1010 |  | RD | Ref1 | DB2013
1013 |  |  |  | 
HPROG1X00100000001D
T0010001DB410B400B44075101000E32019332FFADB2013A00433200857C003B850
E001000
Assume that the instruction is format 3 so we are going to take 6 hexadecimal
8th instruction:
A00433
Since n=0 & i=0, then the instruction is neither format 3 nor format 4
A0 op code => COMPR (format 2) 8th instruction:
A004
COMPR A , S
Op code | ni xbpe | Disp
1010 00 | 00 | 
Symbol | Address
Ref1 | 1026
Ref2 | 100A
Op code | R1 | R2
1010 000 | 0000 | 0100

## Slide 11
 | PROG1 | Start | 1000 | -----------
1000 |  | CLEAR | X | B410
1002 |  | CLEAR | A | B400
1004 |  | CLEAR | S | B440
1006 |  | +LDT | #4096 | 75101000
100A | Ref2 | TD | Ref1 | E32019
100D |  | JEQ | Ref2 | 332FFA
1010 |  | RD | Ref1 | DB2013
1013 |  | COMPR | A,S | A004
1015 |  |  |  | 
HPROG1X00100000001D
T0010001DB410B400B44075101000E32019332FFADB2013A00433200857C003B850
E001000
Assume that the instruction is format 3 so we are going to take 6 hexadecimal
9th instruction:
332008
Since n=1 & i=1, then direct
Since e=0 => format 3
Since b=0 & p=1, then PC relative
TA= disp+PC = 008+1018 = 1020
Op code => return discarded bits
30 op code => JEQ
JEQ Ref3
Op code | ni xbpe | Disp
0011 00 | 11 0010 | hexa (008)
Symbol | Address
Ref1 | 1026
Ref2 | 100A
Ref3 | 1020
Op code | ni xbpe | Disp
0011 0000 | 11 0010 | hexa (008)

## Slide 12
 | PROG1 | Start | 1000 | -----------
1000 |  | CLEAR | X | B410
1002 |  | CLEAR | A | B400
1004 |  | CLEAR | S | B440
1006 |  | +LDT | #4096 | 75101000
100A | Ref2 | TD | Ref1 | E32019
100D |  | JEQ | Ref2 | 332FFA
1010 |  | RD | Ref1 | DB2013
1013 |  | COMPR | A,S | A004
1015 |  | JEQ | Ref3 | 332008
1018 |  |  |  | 
HPROG1X00100000001D
T0010001DB410B400B44075101000E32019332FFADB2013A00433200857C003B850
E001000
Assume that the instruction is format 3 so we are going to take 6 hexadecimal
10th instruction:
57C003
Since n=1 & i=1, then direct
Since e=0 => format 3
Since x=1 => indexed ,X
Since b=1 & p=0, then Base relative
TA= disp+B = 003+101A = 101D
Op code => return discarded bits
54 op code => STCH
STCH Ref4
Op code | ni xbpe | Disp
0101 01 | 11 1100 | hexa (003)
Symbol | Address
Ref1 | 1026
Ref2 | 100A
Ref3 | 1020
Ref4 | 101D
Op code | ni xbpe | Disp
0101 0100 | 11 1100 | hexa (003)

## Slide 13
 | PROG1 | Start | 1000 | -----------
1000 |  | CLEAR | X | B410
1002 |  | CLEAR | A | B400
1004 |  | CLEAR | S | B440
1006 |  | +LDT | #4096 | 75101000
100A | Ref2 | TD | Ref1 | E32019
100D |  | JEQ | Ref2 | 332FFA
1010 |  | RD | Ref1 | DB2013
1013 |  | COMPR | A,S | A004
1015 |  | JEQ | Ref3 | 332008
1018 |  | STCH | Ref4,X | 57C003
101B |  |  |  | 
HPROG1X00100000001D
T0010001DB410B400B44075101000E32019332FFADB2013A00433200857C003B850
E001000
11th instruction:
B850
B8 op code => TIXR (format 2)
TIXR T
Symbol | Address
Ref1 | 1026
Ref2 | 100A
Ref3 | 1020
Ref4 | 101D
Op code | R1 | R2
1011 1000 | 0101 | 0000

## Slide 14
 | PROG1 | Start | 1000 | -----------
1000 |  | CLEAR | X | B410
1002 |  | CLEAR | A | B400
1004 |  | CLEAR | S | B440
1006 |  | +LDT | #4096 | 75101000
100A | Ref2 | TD | Ref1 | E32019
100D |  | JEQ | Ref2 | 332FFA
1010 |  | RD | Ref1 | DB2013
1013 |  | COMPR | A,S | A004
1015 |  | JEQ | Ref3 | 332008
1018 |  | STCH | Ref4,X | 57C003
101B |  | TIXR | T | B850
101D | Ref4 |  |  | 
HPROG1X00100000001D
T0010001DB410B400B44075101000E32019332FFADB2013A00433200857C003B850
E001000
Symbol | Address
Ref1 | 1026
Ref2 | 100A
Ref3 | 1020
Ref4 | 101D